## Slide 1
eSett customer committee, May 7th 2019
Status of Nordic Balancing Model including 15 minutes time resolution

## Slide 2: Development for balancing philosophy
Frequency control
mACE
~0
ACE in each country
~0
~0
~0
~0
~0
~0
~0
~0
~0
~0
~0
~0
~0
~0
~0
mACE
controller
More efficient use of resources
Netting of imbalances
Merit order bid list
Digitalization of balancing
Better control with flows
Clearer responsibilities

## Slide 3: mACE control – efficient trade and netting
Imbalances and available reserves in each bid-area are optimized in a central algorithm. This secures
optimized use of grid capacity
efficient exchange of balancing products
fair settlement between buyers and sellers

## Slide 4
Our goals for the future Nordic power system
Ability to handle major changes in the power system and maintain system security in the short and long term
Efficient integration with European markets and implementation of EU-regulation
Create value and beneficial solutions for all Nordic countries through clear responsibilities and freedom of action for Nordic TSOs
Incentivize development
and modernization towards the
power system
of the future
Strengthening system security in the Nordic
synchronous area, improve efficiency, and harmonize with Europe

## Slide 5: New roles in the Nordic Balancing Model
CSP delivers services to all the Nordic TSOs
CSP responsible for IT development to support the common services
Market design etc. decided jointly by all TSO
Each TSO responsible for local activities
Increased national responsibility compared with current model
National TSOs:
Energinet
Fingrid Statnett
Svenska kraftnät
Common service provider (CSP):
Svenska kraftnät and Statnett
IT development for common services
Common tasks
Dimensioning process
Common aFRR capacity market
Common mFRR capacity market
Common mFRR activation optimization function
Common aFRR activation optimization function
Nordic security function
Price and TSO-TSO cost calculation
Reporting
Transparency
TSO tasks
Collect bids
Settlement TSO-TSO
Settlement BSPs and BRPs
Grid model
Update balancing energy exchange plans
Bottleneck review
Redispatch/internal bottlenecks
Imbalance prognosis
Activation request
Local merit order list and manual bid activation
mFRR ordering
ACE calculation
aFRR controller
aFRR activation towards BSPs

## Slide 6
2018
2019
2020
2021
15 min ISP
New Imbalance Price
Single pricing
M1B - roles
Q2 2020
M2 - aFRR
Q1 2021
Q2 2019
Q4 2019
Q4 2020
Nordic functions
Existing state
New state
European function
M1A - IT
Q1 2020
Common capacity market mFRR.
Common capacity market aFRR.
Nordic AOF for aFRR Energy
ACE based Balancing
NEW settlement of unintended exchange between TSO’s (Scheduled mFRR and aFRR as intended exch.)
Nordic AOF for mFRR
aFRR Energy bids, free bids
MARI
PICASSO
Frequency based Balancing
Balancing Power exchange based on todays principles
Pro-rata aFRR based on frequency
Manual operator decisions from the frequency leader
Trial operation
Balancing Power exchange based on 15 min resolution (TSO-TSO) (Scheduled mFRR as intended)
Partly ACE-based balancing (mFRR)
The road map is subject to change – will be updated

## Slide 7: aFRR Capacity Market
Huge benefits of common capacity market – continues Nordic integration and efficiency
IT development according to plan
Proposal for Nordic aFRR capacity market and cross-zonal capacity allocation methodology submitted to Nordic NRAs for regulatory approval

## Slide 8: Fundamental change in Nordic balancing
From manual processes based om operator knowledge and experience to automated processes. Necessary due to increase in complexity, and requires:
  Extensive change of control room processes
  Formalization of knowledge and routines
  Considerable IT-investments
  Significant improvement in data quality
From control based on balance in synchronous area to control based on balance within each bid-area
  Smaller building blocks a prerequisite for automated processes
  Provides consistency between authority and responsibility between TSOs
  Basis for correct settlement and proper incentives
  Depending on regulatory approvals
From an ambitious roadmap in parallel with other major development in system operation – to an ambitious and realistic plan for implementation.
1.Generation mACE
15 min Time Resolution
2.Generation mACE

## Slide 9: Challenges encountered
We can not add more complexity (e.g smaller bidsize, fluctuations, interconnectors), nor less time (15 minutes time resolution) on the operators without extensive automated operator support
The needed operator support comes with the IT-tools planned in Nordic Balancing Model
Regulation is clear – there is no easy way to be compliant to 15 minutes resolution, without having support for 15 minutes trade

## Slide 10: Timing of 15 minutes resolution in the Nordic region
Implementation of 15 minutes resolution requires extensive automation of processes in the control centers and implementation of 15 min mFRR market.
Changes are also needed within:
  Datahubs
  eSett
  IT-systems of all market participants
  Meters
Massive change for Nordic electricity markets and power system

## Slide 11: Roadmap for NBM including 15 minutes time resolution will be updated
TSOs are updating a joint roadmap for NBM including 15 minutes time resolution. Stakeholders will be consulted during the preparation of the roadmap.
Implementation of AOF (Activation Optimization Function), automatic bid selection and 15min mFRR market are some of the prerequisites before 15 min ISP can be implemented.
New TSO proposal for NBM roadmap will be presented at the stakeholder webinar on May 29.

## Slide 12: Current status of roadmap work
TSOs can now confirm that more time is required for implementation of 15 minutes resolution due to changes of TSO processes.
TSOs can’t decide on postponement of 15 minutes resolution go-live – NRA decision is needed.
Recommendation based on the TSOs work so far and the current understanding: Go-live of 15 minutes resolution requires at least more than a year compared to original road map.

## Slide 13: Current TSO work subject to change
15 minutes resolution
go-live
mFRR market with 15 min process
Trial run
New Nordic aFRR Capacity market go-live Q1/2020
Today’s balancing model
ACE based balancing
New imbalance model
(1-balance/1-price)
15
ISP
NBM Roadmap update
= go-live
TSO operator support – 15 min ISP compliant
= go-live
(TSO internal)

## Slide 14: Stakeholder involvement
Nordic reference group established:
  Purpose
    contribute to the planning of the common Nordic NBM Roadmap
    follow the implementation phase
    identify risks and propose ways to mitigate them
    increase stakeholder awareness of NBM and 15 minutes time resolution
  Members represent a wide range of market participants and are nominated to the group by industry associations of each Nordic country. Regulators are observer members in the group
  First meeting May 21, the aim is to have four meetings per year
Information is published on NBM website http://nordicbalancingmodel.net/
Webinars to be organised on current topics

## Slide 15: Next steps for NBM roadmap update process
TSO replanning
First meeting of NBM reference group 21.5.
stakeholder
consultation
Updated NBM Roadmap considering the stakeholder feedback
NRA process
Solutions Seminar
26.4.
New TSO proposal for NBM roadmap 29.5.
Stakeholder webinar